## Slide 1
Trajectory Generation in High Density Environment
Suvo Ganguli
Alberto Speranzon
Mar 2018
Mid-Term Review

## Slide 2: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Summary of Results
Tradeoff Data and Charts

## Slide 3: Trajectory Generation
There are two steps to the trajectory generation:
  Laplacian Planner Trajectory Generation
    Solves for a potential flow from start point to end point avoiding obstacles
    Does not take into account vehicle dynamics and constraints
    Provides an initial solution for the MPC Trajectory Generator
  MPC Trajectory Generation
    Solves an optimization problem to generate a short trajectory
    Moves one step along the trajectory and resolves the optimization problem
    Takes into account vehicle dynamics and constraints

## Slide 4: MPC Trajectory Generation
Minimize cost
  Velocity error
  Lateral path error
  Control signals
Satisfy vehicle dynamics and constraints
Satisfy other constraints
  Trajectory constraints
  Terminal constraints
  Lateral Acceleration constraint
Laplacian trajectory
MPC trajectory
Trajectory constraints
Terminal constraints
Obstacle
Safety Margin

## Slide 5: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Summary of Results
Tradeoff Data and Charts

## Slide 6: Tradeoff Parameters
Our goal is to trade off the CPU time (CT) with
  Trajectory Parameters
    Number of MPC time steps = N
    MPC time step = T
  Model Complexity
    Number of states = ns
  Obstacle density
    Number of obstacles = no
Model Complexity
  4 state model
  6 state model
Obstacle Density is measured by the number of obstacles which are
  Static
  Placed to obstruct the line of sight from the start point to the end point
N | T (sec) | ns | no
4 | 0.2 | 4 | 0
6 | 0.4 | 6 | 1
8 |  |  | 2
10 |  |  | 
CT
vs

## Slide 7: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Summary of Results
Tradeoff Data and Charts

## Slide 8: Summary of Results
CPU Time (CT) variation with the tradeoff parameters – number of trajectory steps (N), number of obstacles (no) and number of states (ns) are as follows:
  CT increases with N as 2N
  CT increases with no as e-no
  CT decreased from ns = 4 to ns = 6
  CT increases linearly with T
Increase in horizon distance leads to:
  Smoother trajectory
  Increase in comfort level
  Decrease in control effort
  This is because with increase in horizon distance, control action can be taken earlier.
  This is at the cost of increase in computation time (CT)

## Slide 9: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
  Summary of Results
  CPU time vs Number of Time Steps (CT vs N)
  CPU time vs Number of Obstacles (CT vs no)
  CPU time vs Number of States (CT vs ns)
  CPU time vs Time Step (CT vs T)

## Slide 10: Trajectory Variation with No. of Time Steps
With number of states = 4 and number of obstacles = 1, as we increase the number of time steps = 4, 6, 8, we observe that the trajectory gets smoother
  If a “ribbon” being pulled along a circuitous path, the longer the ribbon, the wider the turns.
N = 4
N = 6
N = 8

## Slide 11: CPU Time vs No. of Time Steps (CT vs N)
CPU mean time increases with N as 2N
N=4
N=6
N=8
N=10

## Slide 12: Tradeoff Curves for Design – 1 of 2
Increase in N (equivalent to horizon distance) leads to:
  Smoother trajectory
  Increase in comfort level
  Decrease in control effort
  At the cost of
  Increase in computation time
Computation time
Trajectory Smoothness
Control Effort
Control Effort
1
Comfort Level

## Slide 13: Tradeoff Curves for Design – 2 of 2
The same horizon length can be formed with different combinations of N and T – for e.g., (N = 9, T = 0.4) vs (N = 6, T = 0.6)
Plots below show that control effort and the trajectory smoothness are similar. However the Computation Time is 4X more for (N = 9, T = 0.4)
N=6, T = 0.6
N=6, T = 0.6
N=9, T = 0.4
N=9, T = 0.4
4X

## Slide 14: Tradeoff Curves for Design – 2 of 2
Too large a time step can lead to infeasible solution as the required heading change can be large and the solution for the nonlinear optimization cannot be guaranteed
(N = 9, T = 0.4)
(N = 4, T = 0.9)
requires small heading change
requires large heading change