## Slide 1
Trajectory Generation in High Density Environment
Suvo Ganguli
Alberto Speranzon
Mar 2018
Mid-Term Review

## Slide 2: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
Summary

## Slide 3: Trajectory Generation
There are two steps to the trajectory generation:
  Laplacian Planner Trajectory Generation
    Solves for a potential flow from start point to end point avoiding obstacles
    Does not take into account vehicle dynamics and constraints
    Provides an initial solution for the MPC Trajectory Generator
  MPC Trajectory Generation
    Solves an optimization problem to generate a short trajectory
    Moves one step along the trajectory and resolves the optimization problem
    Takes into account vehicle dynamics and constraints

## Slide 4: MPC Trajectory Generation
Minimize cost
  Velocity error
  Lateral path error
  Control signals
Satisfy vehicle dynamics and constraints
Satisfy other constraints
  Trajectory constraints
  Terminal constraints
  Lateral Acceleration constraint
Laplacian trajectory
MPC trajectory
Trajectory constraints
Terminal constraints
Obstacle
Safety Margin

## Slide 5: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
Summary

## Slide 6: Tradeoff Parameters
Our goal is to trade off the CPU time (CT) with
  Trajectory Parameters
    Number of MPC time steps = N
    MPC time step = T
  Model Complexity
    Number of states = ns
  Obstacle density
    Number of obstacles = no
Model Complexity
  2 states model
  4 state model
  6 state model
Obstacle Density is measured by the number of obstacles which are
  Static
  Placed to obstruct the line of sight from the start point to the end point
N | T (sec) | ns | no
4 | 0.2 | 4 | 0
6 | 0.4 | 6 | 1
8 |  |  | 2
10 |  |  | 
CT
vs

## Slide 7: Model Complexity
4 state model
6 state model

## Slide 8: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
  CPU time vs Number of Time Steps (CT vs N)
  CPU time vs Number of Obstacles (CT vs no)
  CPU time vs Number of States (CT vs ns)
Summary

## Slide 9: Trajectory Variation with No. of Time Steps
With number of states = 4 and number of obstacles = 1, as we increase the number of time steps = 4, 6, 8, we observe that the turn gets wider.
  If a “ribbon” being pulled along a circuitous path, the longer the ribbon, the wider the turns.
N = 4
N = 6
N = 8

## Slide 10: CPU Time vs No. of Time Steps (CT vs N)
CPU mean time increases with N as 2N
N=4
N=6
N=8
N=10

## Slide 11: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
  CPU time vs Number of Obstacles (CT vs N)
  CPU time vs Number of Obstacles (CT vs no)
  CPU time vs Number of Time Steps (CT vs ns)
Summary

## Slide 12: MPC Trajectory in Presence of Obstacles
MPC Trajectory Generator successfully generates path between the start and end point in presence of obstacles
No Obstacle
1 Obstacle
2 Obstacles
N = 8, T = 0.4, ns = 4

## Slide 13: MPC Trajectory Satisfies Vehicle Constraints
Vehicle has a tendency of slowing down during the turns.
MPC constraints prevents the vehicle to slow down too much
N = 4, T = 0.4, ns = 4, no = 2
Corresponds to the turns to avoid the two obstacles

## Slide 14: CPU Time vs Number of Obstacles (CT vs no)
Average CPU time increases with the number of obstacles
The increase exponentially decays with increase in number of obstacles
9x
11x

## Slide 15: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
  CPU time vs Number of Time Steps (CT vs N)
  CPU time vs Number of Obstacles (CT vs no)
  CPU time vs Number of States (CT vs ns)
Summary

## Slide 16: Number of Solver Iterations
CT for ns = 6 takes less time than ns = 4
Number of Solver Iterations for ns = 4 is much more than ns = 6. In fact, for ns = 4, the number of Solver Iterations hits the maximum (100) for several trajectory steps.

## Slide 17: Summary
CPU Time (CT) increases with increase in number of obstacles (no) and number of time steps (N). This is expected.
CPU Time (CT) decreases with increase in number of states (ns). This is unexpected and needs to be studied further.

## Slide 18: Pictures

## Slide 19: Title Slide Picture
Trajectory Generator