## Slide 1
Trajectory Generation in High Density Environment
Suvo Ganguli
Alberto Speranzon
Apr 2018
Mid-Term Review

## Slide 2: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Summary of Results
Tradeoff Data and Charts

## Slide 3: Trajectory Generation
There are two steps to the trajectory generation:
  Laplacian Planner Trajectory Generation
    Provides an initial solution for the MPC Trajectory Generator
    Solves for a potential flow from start point to end point avoiding obstacles
    Does not take into account vehicle dynamics and constraints
  MPC Trajectory Generation
    Solves an optimization problem to generate a short trajectory
    Moves one step along the trajectory and resolves the optimization problem
    Takes into account vehicle dynamics and constraints

## Slide 4: MPC Trajectory Generation
Minimize cost
  Velocity error
  Lateral path error
  Control signals
Satisfy vehicle dynamics and constraints
Satisfy other constraints
  Trajectory constraints
  Terminal constraints
  Lateral Acceleration constraint
Laplacian trajectory
MPC trajectory
Trajectory constraints
Terminal constraints
Obstacle
Safety Margin

## Slide 5: Tradeoff Parameters
Our goal is to trade off the CPU time (CT) with
  Trajectory Parameters
    Number of MPC time steps = N
    MPC time step = T
  Model Complexity
    Number of states = ns
  Obstacle density
    Number of obstacles = no
Model Complexity
  4 state model
  6 state model
Obstacle Density is measured by the number of obstacles which are
  Static
  Placed to obstruct the line of sight from the start point to the end point
N | T (sec) | ns | no
4 | 0.2 | 4 | 0
6 | 0.4 | 6 | 1
8 |  |  | 2
10 |  |  | 
CT
vs

## Slide 6: Summary of Results
CPU Time (CT) variation with the tradeoff parameters – number of trajectory steps (N), number of obstacles (no) and number of states (ns) are as follows:
  CT increases with N as 2N
  CT increases with no as e-no
  CT increases linearly with T
  CT decreased from ns = 4 to ns = 6
Increase in horizon distance leads to:
  Smoother trajectory
  Increase in comfort level
  Decrease in control effort
  This is because with increase in horizon distance, control action can be taken earlier.
  This is at the cost of increase in computation time
Analysis not shown in this slide deck
Key Takeaway

## Slide 7: Trajectory Variation with No. of Time Steps
With number of states = 4 and number of obstacles = 1, as we increase the number of time steps = 4, 6, 8, we observe that the trajectory gets smoother
  If a “ribbon” being pulled along a circuitous path, the longer the ribbon, the wider the turns.
N = 4
N = 6
N = 8

## Slide 8: CPU Time vs No. of Time Steps (CT vs N)
CPU mean time increases with N as 2N as more computation is required for a larger horizon
N=4
N=6
N=8
N=10

## Slide 9: CPU Time vs No. of Obstacles (CT vs no)
1 Obstacle
2 Obstacles
9x
CPU mean time increases with N as k(1-e-bno) as the number of constraints are active for a longer duration

## Slide 10: Using Tradeoff Curves for Design
Increase in N (equivalent to horizon distance) leads to:
  Smoother trajectory
  Increase in comfort level
  Decrease in control effort
  At the cost of
  Increase in computation time
Computation time
Trajectory Smoothness
Control Effort
(V)
Control Effort
(Chidot)
1
Comfort Level
No. of Time Steps (N)
No. of Time Steps (N)
No. of Time Steps (N)

## Slide 11: Conclusion
Mid Term goals are met
  Developed trajectory generation software for obstacle avoidance
  Performed trade-off studies
  Summarized results
Recommendation
  Continue with development for 3D trajectory generation
  Perform trade-off study

## Slide 12: Extra Slides

## Slide 13: Model Complexity
4 state model
6 state model

## Slide 14: Number of Solver Iterations
ns=4
ns=6
ns=4
ns=6
ns=6
(smoother)
ns=4
CT for ns = 6 takes less time than ns = 4 (counter-intuitive)
  For ns = 6, the control reacts faster as the derivative of the acceleration is controlled
  Hence it takes less computation since the change in lateral position of the terminal point is easier to control
  The resultant path is smoother for ns = 6 as the control is more effective

## Slide 15: MPC Trajectory Satisfies Vehicle Constraints
Vehicle has a tendency of slowing down during the turns.
MPC constraints prevents the vehicle to slow down too much
N = 4, T = 0.4, ns = 4, no = 2
Corresponds to the turns to avoid the two obstacles

## Slide 16: Tradeoff Curves for Design – 2 of 3
The same horizon length can be formed with different combinations of N and T – for e.g., (N = 9, T = 0.4) vs (N = 6, T = 0.6)
Plots below show that control effort and the trajectory smoothness are similar. However the Computation Time is 4X more for (N = 9, T = 0.4)
N=6, T = 0.6
N=6, T = 0.6
N=9, T = 0.4
N=9, T = 0.4
4X

## Slide 17: Tradeoff Curves for Design – 3 of 3
Too large a time step can lead to infeasible solution as the required heading change can be large and the solution for the nonlinear optimization cannot be guaranteed
(N = 9, T = 0.4)
(N = 4, T = 0.9)
requires small heading change
requires large heading change