## Slide 1
Trajectory Generation in High Density Environment
Suvo Ganguli
Alberto Speranzon
July, 2018
Final Review

## Slide 2
Agenda
Project Overview – 1 min
Summary of Accomplishments – 15 min
Future Work – 1 min
Q&A – 3 min
Honeywell Internal
Honeywell Internal
Notes: Honeywell Internal
2

## Slide 3
Project Overview
Deliverables
  Mid Term
    Developed 2D trajectory generation algorithm
    Design trade-off studies
  End Term
    Algorithm for avoiding pop-up obstacles
    Alternate 2D trajectory generation software without using costly / time-consuming global planner
    Comparative and robustness studies
Project Summary
  PI: Suvo Ganguli, Alberto Speranzon
  RTC: CNS
  Project Name: Trajectory Generation in High Density Environment
  Budget: 75K
Problem Statement/Objective:
  Trajectory generation in cluttered environment is a key problem to solve for autonomous operations
  The goal of this project is to understand the trade-offs between the different parameters used to design trajectory generation in presence of obstacles
Project Status
  YTD Spend: 75K
  WORK Complete: 100%
Honeywell Internal
Notes: Honeywell Internal
3

## Slide 4: Basic Concepts
Local Planner – generates trajectory for a finite path
  MPC (Model Predictive Control)
Global Planner – generates trajectory from start to end point
  Laplacian
  MPC
MPC generates a trajectory
  By solving an optimization problem for multiple time steps in future
  Taking a single time step, and repeating optimization
  Takes into account vehicle dynamics
Laplacian generates a trajectory
  Assigning high potential to start point, obstacles and low potential to end point
  Finding optimal path along the steepest gradient
  Does not take into account vehicle dynamics
Global Planner
Local Planner
o
o
o
o
o
o
o
o
MPC
+
+
-
Laplacian

## Slide 5: Mid Term Accomplishments
Trajectory Generation Algorithm:
  Local Planner – MPC
  Global Planner – Laplacian
  Obstacles known a priori
Design Tradeoffs (key result):
  CPU time vs No. of Time Steps
  Trajectory smoothness vs No. of time steps
Computation time
No. of Time Steps (N)
Trajectory Smoothness
No. of Time Steps (N)
Obstacle with safety margin
Laplacian path
MPC path

## Slide 6
End Term Accomplishments
Honeywell Internal
Trajectory Generation Algorithm
  Obstacles not known a priori
  Global Planner (only) – MPC
  Advantage
    Avoid costly re-computation of Laplacian planner (2X-3X reduction)
Robustness Study
  100 test cases with 10 obstacles (pop-up)
  99 out of 100 test cases successfully generated trajectory
  Specific test cases to analyze occasional failure
Field of View
Obstacles with Safety Margin
MPC Path
MPC Horizon
Notes: Honeywell Internal
6

## Slide 7
Honeywell Internal
MPC Randomized Test Cases
MPC Trajectory Generator changes the heading of the path upon finding less “costly” path
MPC Trajectory Generator relative heading constraint is changed from 90 deg to 30 deg when no obstacles are in view
Notes: Honeywell Internal
7

## Slide 8
MPC Randomized Test Cases
Honeywell Internal
MPC Trajectory Generator is trapped and unable to progress farther.
It turns right to follow the less “costly” path until it views another obstacle for which no feasible path can be generated.
MPC Trajectory Generator changes the heading of the path upon a “dead end”
Would have lead to longer trajectory
causes infeasibility
Notes: Honeywell Internal
8

## Slide 9
MPC Specific Test Cases
Honeywell Internal
MPC Trajectory Generator is trapped and slows down to zero speed due to tighter turn constraint
MPC Trajectory Generator successfully reaches the end point with relaxed turn constraints
Tighter turn constraint
Relaxed turn constraint
Notes: Honeywell Internal
9

## Slide 10
Future Work
Modify algorithm to maintain a family of feasible paths:
  Modify problem formulation to allow velocity reversal
  Continue on the MPC path computed in the previous time step and run a less costly global planner (e.g., Probabilistic Road Maps) to re-initialize the MPC problem
Optimize algorithm to run in real time.
  Use near-optimal values to reduce the number of iterations
  Use efficient linear solvers which is used by the nonlinear optimizer
Honeywell Internal
Notes: Honeywell Internal
10

## Slide 11
Q&A
Honeywell Internal
Notes: Honeywell Internal
11