## Slide 1
Trajectory Generation in High Density Environment
Suvo Ganguli
Alberto Speranzon
Feb 2018
Mid-Term Review

## Slide 2: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
Summary

## Slide 3: Trajectory Generation
There are two steps to the trajectory generation:
  Laplacian Planner Trajectory Generation
    Solves for a potential flow from start point to end point avoiding obstacles
    Does not take into account vehicle dynamics and constraints
    Provides an initial solution for the MPC Trajectory Generator
  MPC Trajectory Generation
    Solves an optimization problem to generate a short trajectory
    Moves one step along the trajectory and resolves the optimization problem
    Takes into account vehicle dynamics and constraints

## Slide 4: MPC Trajectory Generation
Minimize cost
  Velocity error
  Lateral path error
  Control signals
Satisfy vehicle dynamics and constraints
Satisfy other constraints
  Trajectory constraints
  Terminal constraints
  Lateral Acceleration constraint
Laplacian trajectory
MPC trajectory
Trajectory constraints
Terminal constraints
Obstacle
Safety Margin

## Slide 5: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
Summary

## Slide 6: Tradeoff Parameters
Our goal is to trade off the CPU time (CT) with
  Trajectory Parameters
    Number of MPC time steps = N
    MPC time step = T
  Model Complexity
    Number of states = ns
  Obstacle density
    Number of obstacles = no
Model Complexity
  2 states model
  4 state model
  6 state model
Obstacle Density is measured by the number of obstacles which are
  Static
  Placed to obstruct the line of sight from the start point to the end point
N | T (sec) | ns | no
4 | 0.2 | 4 | 0
6 | 0.4 | 6 | 2
8 | 0.6 |  | 2
10 |  |  | 
CT
vs

## Slide 7: Model Complexity
4 state model
6 state model

## Slide 8: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
  CPU time vs Number of Time Steps (CT vs N)
  CPU time vs Number of Obstacles (CT vs no)
  CPU time vs Number of States (CT vs ns)
Summary

## Slide 9: Trajectory Variation with No. of Time Steps
With number of states = 4 and number of obstacles = 1, as we increase the number of time steps = 4, 6, 8, we observe that the turn gets wider.
  If a “ribbon” being pulled along a circuitous path, the longer the ribbon, the wider the turns.
N = 4
N = 6
N = 8

## Slide 10: CPU Time vs No. of Time Steps (CT vs N)

## Slide 11: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
  CPU time vs Number of Obstacles (CT vs N)
  CPU time vs Number of Obstacles (CT vs no)
  CPU time vs Number of Time Steps (CT vs ns)
Summary

## Slide 12: MPC Trajectory in Presence of Obstacles
MPC Trajectory Generator successfully generates path between the start and end point in presence of obstacles
No Obstacle
1 Obstacle
2 Obstacles
N = 4, T = 0.4, ns = 4

## Slide 13: MPC Trajectory Satisfies Vehicle Constraints
N = 4, T = 0.4, ns = 4, no = 2
Corresponds to the turns to avoid the two obstacles

## Slide 14: CPU Time vs Number of Obstacles (CT vs no)
Average CPU time increases (in general) with the number of obstacles
Average CPU time is increases with the number of MPC time steps
3x
9x
11x

## Slide 15: CPU Time vs Number of Obstacles (CT vs no)
CPU Time varies with the number of iterations. So, averaging over several runs will be more representative of CT vs no.
In case of N = 4, the trajectory generator hits less constraints once it passes the 2nd obstacle (due to the shorter horizon). This leads to slightly less average CT compared to the case with 1 obstacle.
constraints for final leg of trajectory is inactive for N=4

## Slide 16: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
  CPU time vs Number of Time Steps (CT vs N)
  CPU time vs Number of Obstacles (CT vs no)
  CPU time vs Number of States (CT vs ns)
Summary

## Slide 17: Overview
Trajectory Generation in 2-dimensional space
  Laplacian Planner
  Model Predictive Control (MPC)
Tradeoff Parameters
Tradeoff Data and Charts
  CPU time vs Number of Obstacles (CT vs N)
  CPU time vs Number of Obstacles (CT vs no)
  CPU time vs Number of Time Steps (CT vs ns)
Summary

## Slide 18: CPU Time vs Number of States (CT vs ns)
With number of time steps = 4, and number of states = 4, we get instability. This is due to relatively shorter horizon. Plus, the control is instead of which results in slower response.
With number of time steps = 4, and number of states = 6, the trajectory cannot negotiate the turn. This is due the relatively shorter horizon (N).
ns = 4
ns = 6

## Slide 19: CPU Time vs Number of States (CT vs ns)
With number of time steps = 6, and number of states = 4 and 6, we can reach the end point when we make the following changes:
  Reduce the lateral error margin for the terminal point
  Add a terminal velocity constraint
ns = 4
ns = 6

## Slide 20: CPU Time vs Number of States (CT vs ns)
The CPU time is less for ns = 6 as compared to ns = 4. This is counter-intuitive and needs to be studied further.
Possible Explanation:
  Number of active constraints are less for ns = 6
  But that did not turn out to be correct (see next slide).
-- ns = 4, -- ns = 6
no = 0
no = 1
no = 2
Number of variables = N.(ns + nu)
Number of constraints = 2N + 3

## Slide 21: Constraints for 1 Obstacle
State and control constraints are not active in these cases
Path constraints are almost always active due to the narrow terminal constraint on lateral error for both ns = 4 and 6
Constraint on terminal velocity is active for slightly more time for ns = 6 than ns = 4. This does not explain why CT for ns = 6 is less than ns = 4
N = 6, T = 0.4, ns = 4
N = 6, T = 0.4, ns = 6
Terminal velocity constraint is active for longer time for ns = 6

## Slide 22: Number of Solver Iterations
Number of Solver Iterations for ns = 4 is much more than ns = 6. This explains why CT for ns = 6 takes less time than ns = 4
Possible explanation (needs to be checked):
  Weight on Vdot control for ns = 4 is effectively less than Vddot for ns = 6

## Slide 23: Summary
CPU Time (CT) increases with increase in number of obstacles (no) and number of time steps (N). This is expected.
CPU Time (CT) decreases with increase in number of states (ns). This is unexpected and needs to be studied further.

## Slide 24: Pictures

## Slide 25: Title Slide Picture
Trajectory Generator