## Slide 1
Trajectory Generation in High Density Environment
Suvo Ganguli
Alberto Speranzon
Aug 01, 2018
Final Review

## Slide 2: Trajectory Generation in High Density Environment
Project Description
  Trajectory generation in cluttered environment is a key problem to solve for autonomous operations
  The goal of this project is to understand the trade-offs between the different parameters used to design trajectory generation in presence of obstacles
Planned Deliverables
    - Develop 2D trajectory generation algorithm
      Perform design trade-off studies
    - Develop alternate 2D trajectory generation algorithm which is computationally efficient
      Perform comparative and robustness studies
Team Members
  Suvo Ganguli
  Alberto Speranzon

## Slide 3: Basic Concepts
Local Planner – generates trajectory for a part of the path. Example:
  MPC (Model Predictive Control)
Global Planner – generates trajectory from start to goal point. Example:
  Laplacian
  MPC
MPC Planner generates a trajectory by
  Solving an optimization problem for multiple time steps in future
  Taking a single time step, and repeating optimization
  Does take into account vehicle kinematics and constraints
Laplacian Planner generates a trajectory by
  Assigning +1 potential to start point, zero potential to obstacles and -1 potential to goal point
  Finding optimal path using gradient descent
  Does not take into account vehicle kinematics and constraints
Global Planner
Local Planner
o
o
o
o
o
o
o
o
MPC
+1
0
-1
Laplacian
Time Step k
Time Step k+1

## Slide 4: Approach 1 (Mid Term)
Global planner – Laplacian
Local planner – MPC
Algorithm:
Compute Laplacian path from start to goal point
At every MPC time step, set final point in the horizon is “near” the Laplacian path
Use the first point in the horizon to generate the next point of the final path
Result: Final path from start to goal point satisfies vehicle dynamics and constraints (since MPC path does)
Laplacian path
Boundary for terminal point
MPC path at time step k
Final path point
Obstacle with safety margin
Laplacian path
MPC path
Current location
Boundary for all points

## Slide 5: MPC Problem Setup
Minimize cost function with following components:
  Sum of
    Distances of MPC trajectory points from Laplacian trajectory (state cost)
    Velocity errors (state cost)
    Accelerations (control cost)
    Heading Rates (control cost)
Subject to constraints:
  Vehicle kinematics (nonlinear)
  Control limits for all trajectory points
  Distance of MPC trajectory points from Laplacian trajectory (narrower for terminal point)
  Lateral acceleration
  Limit of velocity errors
Corresponds to two turns to avoid two obstacles

## Slide 6: Tradeoff Parameters
Our goal is to trade off the following
  Computation Time
    averaged over the entire simulation
  Trajectory Smoothness
    cornering distance
  Control Effort
    integrated acceleration and heading rate
  Comfort Level
    1/integrated acceleration
with
  Number of MPC time steps (N)
  Number of Obstacles (no)
Tradeoffs
  Computation time (CT) increases with N (CT ~ 2N)
  Computation time increases with no (CT ~ 1- k.e-b.no)
    For a specific size and location of obstacles
N = 6
N = 8
wider turn
(smoother trajectory)

## Slide 7: Summary of Design Tradeoffs
Increase in N (equivalent to horizon distance) leads to:
  Smoother Trajectory
  Decrease in Control Effort
  Increase in Comfort Level
  At the cost of
  Increase in Computation Time
Computation time
Trajectory Smoothness
Control Effort
(acceleration)
Control Effort
(heading rate)
1
Comfort Level
No. of Time Steps (N)
No. of Time Steps (N)
No. of Time Steps (N)

## Slide 8: Approach 2 (Final Term)
Global and local planner – MPC
MPC problem minimizes the cost function with following components:
  Velocity errors for all points
  Accelerations for all points
  Heading rate of all points
  Relative heading of the goal point w.r.t. the terminal point of the MPC horizon
  Distance between the goal point and the terminal point of the MPC horizon
MPC constraints include
  Limits on acceleration and heading rate
  Distance between MPC points and obstacle greater than radius of safe region around obstacle
  Maximum heading error of terminal point
L
L  0
 0
di > r, i = 1, 2…, N
r
di

## Slide 9: Analysis with 2nd Approach
Comparison with 1st Approach
  Can avoid obstacles not known a priori
  Does not need a separate global planner
  Avoid costly re-computation of Laplacian planner (2X-3X reduction, more reduction with larger grids)
Robustness Study
  100 test cases with 10 obstacles (pop-up)
  99 out of 100 test cases successfully generated trajectory
  Specific test cases to analyze occasional failure
Honeywell Internal
Field of View
Obstacles with Safety Margin
MPC Path
MPC Horizon
Avoid getting trapped
Obstacle 3
Obstacle 1
Notes: Honeywell Internal
8

## Slide 10
Honeywell Internal
MPC Randomized Test Cases
MPC Trajectory Generator changes the heading of the path upon finding less “costly” path
MPC Trajectory Generator relative heading constraint reduces from 90 deg when no obstacles are in view
Notes: Honeywell Internal
9

## Slide 11
MPC Randomized Test Cases
Honeywell Internal
MPC Trajectory Generator is trapped and unable to progress farther.
It turns right to follow the less “costly” path until it views another obstacle for which no feasible path can be generated.
MPC Trajectory Generator changes the heading of the path upon a “dead end”
Would have lead to longer trajectory
causes infeasibility
Obstacle 3
Notes: Honeywell Internal
10

## Slide 12
MPC Specific Test Cases
Honeywell Internal
MPC Trajectory Generator is trapped and slows down to zero speed due to tighter turn constraint
MPC Trajectory Generator successfully reaches the goal point with relaxed turn constraints
Tighter turn constraint
Relaxed turn constraint
Notes: Honeywell Internal
11

## Slide 13: Project Results versus Objectives
Describe the project results and compare the results to the original objectives
Use graphics and photographs as much as possible
Describe the intellectual property created and how it has been protected (WIDS, patent application, trade secret, etc.)
Approx. 10 minutes

## Slide 14: What’s Next for This Technology
WIDS
  Dynamically Feasible Trajectory Generator
    Dynamic feasibility is not considered in many traditional algorithms
    Novel combination of MPC and Laplacian trajectory generation to achieve dynamically feasible trajectory
Expand the technology to include
  3D trajectory generation with application to UAVs
  Dynamic obstacles
  Efficient path re-rerouting upon hitting dead-ends (using Probabilistic Road Maps)
  Obtained IR&D funding to continue development
Optimize the software for real-time application
Questions?